## Slide 1: ECE477 MIDTERM DESIGN REVIEW: TEAM 16
<Add team picture or relevant project picture here>
Notes: Jason

## Slide 2: OUTLINE
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions
Notes: Jason

## Slide 3: PROJECT OVERVIEW
Smart Conveyor Belt System
Sorts packages to different compartments based on barcode information.
More accurate by using 2D barcode scanner
Easy to implement, low maintenance cost
Gentle sorting mechanics protects fragile packages
Customizable sorting rules
Notes: Jason

## Slide 4: PSSCS
An ability to interface with a/multiple barcode scanners
An ability to control all servo positions using level-shifted pwms of variable duty cycle originating from the mcu.
An ability to interface with a motor driver so that our microcontroller can control movement of the conveyor belt.
An ability to interface with an IR sensor in order to detect a package location
An ability to rapidly switch sorting positions to organize packages using microcontroller signals and logic with minimal runtime.
Notes: Jason

## Slide 5: MAJOR COMPONENTS
Microcontroller (MCU) + Servo Motors
STM32F0 Discovery:
Internal clock 48 MHz
2 UART connections
11 timers
I2C connections
Interface with and commands
all other components
Servo Motor (3V-7V) [MG995]:
Strong Torque
Operational Voltage: 3.0V - 7.2V
Stall Torque:12 kg.cm@ 6V, 13kg.cm@7.2V
Rotates flaps to sort parcels
Notes: zi

## Slide 6: MAJOR COMPONENTS
DC Motor
NPC-T74:
24V, ~4A (no-load)
  Will run at 12V
240 RPM
1.09 HP Peak
  Need ~0.1 HP
Drives Conveyor Belt to move
parcels through system
Notes: zi
@24 V draws 4A will be operating at 12V
More than sufficient for our project need

## Slide 7: MAJOR COMPONENTS
Sensors
Barcode Scanner [14810]:
1D/2D code reader. e.g. QR code
Works in the dark
(5V at 135 mA)
Utilizes UART
Reads and delivers parcel barcode information to MCU
Distance Sensor [TOF10120]:
3V - 5 V at 35mA
UART + I2C
Oper. Dist. 100 - 1800mm
Monitor distances of parcels
Notes: Zi
transition

## Slide 8: MAJOR COMPONENTS
Logic Level Shifter + Electronic Speed Controller (ESC)
Logic Level Shifter [709804]:
Bi-Directional
Steps 3.3V signals to 5V signals
  VCCA side voltage range: 1.2V-3.6V;
  VCCB side voltage range: 1.65V-5.5V
Takes in signals from MCU at 3.3V and outputs signals at 5V
Electronic Speed Controller [217-8080]:
12V Nominal voltage
60A continuous current rating
Controlled via PWM or CAN
Control the speed of DC motor that drives conveyor belt
Notes: Jonah

## Slide 9: BLOCK DIAGRAM
Notes: Jonah

## Slide 10: PACKAGING DESIGN
1.
2.
3.
5.
4.
1) Motor plus belt
2) Sprocket connecting belt to roller
3) Servo + Bumper
4) Barcode Scanner
5) Microcontroller and PCB case
1.2 m
1.3 m
1 m
20.32 cm
Notes: Ryan
Include one or more images of your packaging design here. Include relevant dimensions and how you are planning to manufacture your product packaging.

## Slide 11: Packaging

## Slide 12: Packaging Design

## Slide 13: ELECTRICAL SCHEMATIC ELECTRICAL SCHEMATIC
Notes: Jonah
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 14: PCB LAYOUT
Width: 4.399in
Height: 4.487in
Hole Diameter: 0.25in
Notes: Jonah
Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 15: PROTOTYPING PROGRESS
Component | Status
Distance Sensor | Testing In Progress
MCU | 
DC Motor | 
Electronic Speed Controller | 
Barcode Scanner | 
Servo Motor | 
Conveyor Belt | Not implemented yet
Status LED | 
Enable Button | 
Notes: Ryan

## Slide 16: SOFTWARE DEVELOPMENT STATUS
Not Yet Started | In Development
Sorting Algorithm | Reading distance sensor information
Look up table | Reading & sending barcode to MCU
Notes: Ryan

## Slide 17: PROJECT TIMELINE
WEEK 9
Testing of level shifter and making sure microcontroller produces correct PWM signal to drive servo motors
WEEK 10
Testing conveyor belt framework for future integration of mechanical and electrical parts
WEEK 11
Testing Barcode scanner functionality and maximum speed of reception
WEEK 12
Testing distance sensor and the I2C interface
WEEK 13
Integration of DC motor and conveyor belt frame
WEEK 14
Integration of servo motor, level shifter, sorting flaps with the conveyor frame.
WEEK 15
Trials of full system without real parcels first with belt running, then run the full system with full capacity
WEEK 16
More full operation trials and product function demonstration
Notes: Zi

## Slide 18: 3D PRINTING
Questions?